## Slide 1: Transport Protocols in the Internet
Introduction to TCP
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: TCP - Transmission Control Protocol
TCP is the main transport protocol of the Internet
TCP provides
  Reliable end-to-end byte stream over an unreliable network service
Motivation: network with connectionless service
  Packets and messages may be
    duplicated, in wrong order, faulty
    i.e., with such service only, each application would have to provide recovery
      error detection and correction
  Network or service can
    impose packet length
    define additional requirements to optimize data transmission
    i.e., application would have to be adapted

## Slide 3: TCP Characteristics
Data stream oriented
  TCP transfers serial byte stream
  Maintains sequential order
Unstructured byte stream
  Application often has to transmit more structured data
  TCP does not support such groupings into (higher) structures within byte stream

## Slide 4: TCP Characteristics
Data stream oriented
  TCP transfers serial byte stream
  Maintains sequential order
Unstructured byte stream
  Application often has to transmit more structured data
  TCP does not support such groupings into (higher) structures within byte stream
Buffered data transmission
  Byte stream not message stream: message boundaries are not preserved
    no way for receiver to detect the unit(s) in which data were written
  For transmission the sequential data stream is
    Divided into segments
    Delayed if necessary (to collect data)

## Slide 5: TCP Characteristics
Virtual connection
  Connection established between communication parties before data transmission
Two-way communications (fully duplex)
  Data may be transmitted simultaneously in both directions over a TCP connection
Point-to-point
  Each connection has exactly two endpoints

## Slide 6: TCP State machine
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Send SYN
Recv SYN ACK
Send ACK
Send FIN
Recv ACK
Recv FIN Send ACK
Timeout
Send FIN
Recv SYN
Send SYN ACK
Recv FIN
Send ACK
Recv ACK
Timeout
Recv RST
Recv SYN Send SYN ACK
Send FIN
Recv FIN Send ACK
Recv FIN ACK
Send ACK
Recv ACK
Send SYN

## Slide 7: Typical State Sequence of a TCP Client
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Send SYN
Recv SYN,ACK
Send ACK
Send FIN
Recv ACK
Recv FIN, Send ACK
Timeout

## Slide 8: Typical State Sequence of a TCP Server
CLOSED
LISTEN
SYN RCVD
SYN SENT
ESTABLISHED
FIN WAIT 1
FIN WAIT 2
CLOSING
TIME WAIT
CLOSE WAIT
LAST ACK
Timeout
Recv SYN
Send SYN,ACK
Recv ACK
Recv FIN,
Send ACK
Send FIN

## Slide 9: TCP: Message Format
TCP/IP Header Format
Destination Address
Source address
Time to live
Protocol
Header checksum
Identification
D
M
Fragment offset
Version
IHL
Type of service
Total length
PRE
ToS
Data
Options
Source port
Destination port
Sequence number
Piggyback acknowledgement
THL
F
Window
S
R
P
A
U
unused
Checksum
Urgent pointer
Options (0 or more 32 bit words)
IP header
TCP header
Used for demultiplexing:
identifies connection
Used for demultiplexing:
service address for connection setup

## Slide 10: TCP Characteristics
Virtual connection
  Connection established between communication parties before data transmission
Two-way communications (fully duplex)
  Data may be transmitted simultaneously in both directions over a TCP connection
Point-to-point
  Each connection has exactly two endpoints
Reliable
  Fully ordered, fully reliable
    Sequence maintained
    No data loss, no duplicates, no modified data

## Slide 11: TCP in Use & Application Areas
Benefits of TCP
Reliable data transmission
  Efficient data transmission despite complexity
  Can be used with LAN and WAN for
    low data rates (e.g. interactive terminal) and
    high data rates (e.g. file transfer)
Disadvantages when compared with UDP
Higher resource requirements
  buffering, status information, timer usage
Connection set-up and disconnect necessary
  even with short data transmissions
Applications
everything on the Web including video-on-demand (http)
File transfer (scp, ftp)
Interactive terminal (ssh, telnet)
E-mail (smtp, imap)
X-Windows

## Slide 12: Transport layer
Terminology
IN2140: Introduction to Operating Systems and Data Communication

## Slide 13: Terminology: bandwidth (1/2)
Mirriam-Webster online ( http://www.m-w.com ):
Main Entry: band*width, Pronunciation: 'band-"width Function: noun, Date: circa 1937
  1 : a range within a band of wavelengths, frequencies, or energies; especially : a range of radio frequencies which is occupied by a modulated carrier wave, which is assigned to a service, or over which a device can operate
  2 : the capacity for data transfer of an electronic communications system <graphics consume more bandwidth than text does>; especially : the maximum data transfer rate of such a system
Unit: definition 1 - “Hz“, definition 2 - “bit/s“ (bps)
Common terminology in computer network context: How many bits/sec can be transferred = “how thick is the pipe”
Traditional, “real“ definition!
“Information rate“

## Slide 14: Terminology: bandwidth (2/2)
Various wooly “bandwidth“ terms
  Nominal bandwidth: Bandwidth of a link when there is no traffic
  Available bandwidth: (Nominal bandwidth - traffic) ... during a specific interval
  Bottleneck bandwidth: smallest nominal bandwidth along a path, but sometimes also smallest available bandwidth along a path
Throughput: bandwidth seen by the receiver
Goodput: bandwidth seen by the receiving application
  e.g. TCP: goodput != throughput
  Difference is not only message headers - more required to ensure reliability, ordering, flow control, congestion control, ...
Notes: Nominell – tilgjengelig – flaskehals
Flytkontroll - metningkontroll

## Slide 15: Terminology: delay
Propagation delay - time to transfer a bit
Latency = propagation delay + msg_length / bottleneck bandwidth
+ queuing delay
  just a rough measure; e.g., processing delay can also play a role, esp. in core routers (CPU = scarce resource!)
Jitter - delay fluctuations, very critical for most real-time applications
End-to-end delay – time a message needs from a sending entity to a receiving entity
  end-to-end delay on the application layer includes TCP retransmissions
  end-to-end delay on the transport layer does not
Round-trip time (RTT) - time a messages needs to go from sender to receiver and back

## Slide 16: Transport layer
TCP reliability
IN2140: Introduction to Operating Systems and Data Communication

## Slide 17: TCP Reliability
TCP/IP has only two tools for ensuring reliable transfer:
  detecting duplicate byte ranges
  retransmitting data that has not arrived and not arrived correctly

## Slide 18: TCP Reliability
TCP/IP Retransmits segments until they are acknowledged
ACK field is used for that
Destination Address
Source address
Time to live
Protocol
Header checksum
Identification
D
M
Fragment offset
Version
IHL
Type of service
Total length
PRE
ToS
Data
Options
Source port
Destination port
Sequence number
Piggyback acknowledgement
THL
F
Window
S
R
P
A
U
unused
Checksum
Urgent pointer
Options (0 or more 32 bit words)
IP header
TCP header
Acknowledgement:
Next expected byte
Indicator:
Is the ACK field in use

## Slide 19: TCP ACK and Reliability
In modern TCP implementations,
a lot is done to suppress spurious retransmissions.
The reason is that timeouts have another meaning: congestion
Seq=92, 8 bytes data
X
ACK=100
Loss!
Seq=92, 8 bytes data
Timer
start
Timeout!
ACK=100
time
time
Seq=92, 8 bytes data
Seq=92, 8 bytes data
Timer for 92
Timeout!
ACK=100
time
time
Seq=100, 20 bytes data
ACK=120
ACK=120
Seq=120, 10 bytes data
Timer for 100
Timeout retransmission
Spurious retransmission
Notes: Spurious = uberettiget

## Slide 20: TCP Round trip time and timeout
How to set the retransmission timer?
  Must be longer than round-trip time (RTT)
  Too short: many spurious retransmissions
  Too long: slow reaction, flow control buffer fills up
Idea
  Estimated RTT
    Use a SampleRTT: Measure time from segment sending and ACK received
    Compute EstimatedRTT as a floating average
    Increase the EstimatedRTT with a safety margin that is big when SampleRTT changes a lot
      (because fewer timeouts are considered better)
Not only 1 RTT because we have also “Fast Retransmission” for fixing packet loss, explained with “Congestion”

## Slide 21: Transport layer
Flow Control
IN2140: Introduction to Operating Systems and Data Communication

## Slide 22: Flow Control on Transport Layer
Flow control mechanisms:
Stop-and-wait
Sliding window
  Go-back-N / no buffer allocation
  Selective repeat / static buffer allocation
  Credit mechanism / dynamic buffer allocation
Network
Layer
Transport
Layer
Application
Layer
Data Link
Layer
Physical
Layer
Fast sender shall not flood slow receiver
Link layer
Few connections (one per host)
Short distances
Transport layer
Potentially many connections (several per application)
Potentially long distances

## Slide 23: Flow control and error treatment
Problem
sender can send faster than receiver can receive
Without flow control
receiver loses packets despite error-free transmission
With flow control
sender can adapt to receiver’s abilities by feedback
Comment
error control and flow control are usually interlinked
rate control
  controls sending speed as well
  but defines sequencing of send operations
  whereas flow control defines conditions for next send operation
© Ralf Steinmetz, Technische Universität Darmstadt

## Slide 24: Transport layer
Flow Control: stop-and-wait
IN2140: Introduction to Operating Systems and Data Communication

## Slide 25: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
packet
ACK
Needed:
(A) a receiving buffer
(B) bi-directional communication

## Slide 26: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
Packets can get lost
sender
receiver
packet
ACK
packet
Features required by Stop-and-Wait:
fix the loss
distinguish packet loss and ACK loss

## Slide 27: Flow control: Stop-and-Wait
sender
receiver
packet
ACK
(a) fix the loss
packet
start a timer
timer expired
send packet again
start new timer
ACK arrived
cancel timer
Timeout interval:
Too short: unnecessary sending of packets
Too long: unnecessary long wait in case of error

## Slide 28: Flow control: Stop-and-Wait
sender
receiver
(b) distinguish packet loss and ACK loss
sender
receiver
packet 0
ACK
packet 0
packet 0 or
packet 1?
ACK
packet 0 or
packet 1?
ACK
packet 1 expected
packet 0
expected
packet 0
expected
packet 1 expected

## Slide 29: Flow control: Stop-and-Wait
sender
receiver
Distinguish cases by sequence number: single bit with value 0 and 1
sender
receiver
packet 0
expected
packet 0 expected
received
packet 1 expected
received
received 1
0
0
1
0
1
packet
ACK
packet
ACK
0
0
1
0
1
0
ACK
packet
packet
packet
ACK
packet
ACK
packet 1
expected
packet 0
expected
received 0
discard 0
packet 0 expected
packet 1 expected

## Slide 30: Flow control: Stop-and-Wait
Stop-and-Wait
sender can never send new packet before ACK or timeout
connection is idle most of the time
poor throughput
Gigabit Ethernet channel
transmission rate: 1 Gbps
roundtrip delay 200 (2*0.1 )
packet size: 8000 bit
in comparison  ACK is short and negligible
this means
sending takes 8000 bit / 1.000.000.000 bps = 8
sender is blocked for 192 of 200
 Channel utilization 4%
receiver
ACK
packet
sender
s
s

## Slide 31: Transport layer
Flow Control: sliding window
IN2140: Introduction to Operating Systems and Data Communication

## Slide 32: Flow control: Sliding Window
Improve utilization: pipelining
Flow control: sliding window mechanism
sender
receiver
packet 0
ACK 0
packet 1
packet 2
ACK 1
ACK 2
packet 8
ACK 8

## Slide 33: Sliding Window: Concept
1st goal of link flow control:
receiver buffer must not overflow
Assumptions:
each buffer can contain one packet
Two windows per communication relationship
Sender Window (or Send Window)
packets that were sent but not yet acknowledged
Receiver Window (or Receive Window)
packets that can be accepted
w
e
s
e
n
d
s
o
m
e
d
a
t
a
f
r
o
m
t
h
e
t
o
p
send
w
e
s
e
recv
buffers that fit into the current send window can be in flight at the same time
(“in flight”: sent but not acknowledged)
d
s
n
packets that fit into the current receive window
are considered valid and are acknowledged on arrival
packets are identified by sequence numbers
but the packets keep coming
and these numbers will wrap eventually
Notes: flood : overflomme

## Slide 34: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
advancing sender seqno (modulo 8)
LB: when ACK is received
UB: when sending a packet
Sender side
2 variables
LB
UB
0
0
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
0
0

## Slide 35: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
increase UB (modulo 8 !)
when sending a packet
Sender side
2 variables
LB
UB
0
0
send packet(0) packet(1) packet(2) WS=3
1
2
3
increase LB (modulo 8 !)
when receiving an ACK
recv ACK(0): WS=2
1

## Slide 36: Sliding Window: Concept
Sender
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: oldest seqno that is still unconfirmed
UB: next seqno to be sent
if LB==UB : nothing is in flight sender is idle
increase UB (modulo 8 !)
when sending a packet
Sender side
2 variables
LB
UB
send packet(0) packet(1) packet(2) WS=3
3
increase LB (modulo 8 !)
when receiving an ACK
recv ACK(0): WS=2
1
send packet(3) WS=3
4
recv ACK(1), ACK(2), ACK(3) WS=0
2
3
4
send packet(4) packet(5) packet(6) WS=3
5
6
7

## Slide 37: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: lowest valid seqno that should be ACKed
UB: lowest invalid seqno
if UB==LB: buffer full
if UB==(LB+3)%8: nothing to ACK
increase UB (modulo 8 !)
when sending an ACK
Receiver side
2 variables
LB
UB
0
recv packet(0) … WS=2
3
increase LB (modulo 8 !)
when receiving a packet
send ACK(0) WS=3
1
4

## Slide 38: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
lower bound
upper bound
LB: lowest valid seqno that should be ACKed
UB: lowest invalid seqno
if UB==LB: buffer full
if UB==(LB+3)%8: nothing to ACK
increase UB (modulo 8 !)
when sending an ACK
Receiver side
2 variables
LB
UB
recv packet(0) … WS=2
increase LB (modulo 8 !)
when receiving a packet
send ACK(0) WS=3
1
4
recv packet(1) packet(2) packet(3) WS=0
5
6
7
2
3
4
send ACK(1) ACK(2) ACK(3) WS=3

## Slide 39: Transport layer
Flow Control: cumulative ACK
IN2140: Introduction to Operating Systems and Data Communication

## Slide 40: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
0
0
LB
UB
3
0
packet 0
packet 1
packet 2
3
1
ACK 0
4

## Slide 41: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
3
0
LB
UB
4
3
packet 0
packet 1
packet 2
ACK 0
ACK 1
ACK 2
ACK 0
3
6
3

## Slide 42: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
6
0
LB
UB
6
3
packet 0
packet 1
packet 2
ACK 1
ACK 2
ACK 0
3
3
packet 3
packet 4
packet 5
6

## Slide 43: Sliding Window: Concept
Receiver
1
2
5
6
0
3
4
7
Example:
SeqNo: [0..7]
Window Size (WS): 3
Feature: Cumulative ACK
sender
receiver
Sender
1
2
5
6
0
3
4
7
LB
UB
3
0
LB
UB
7
3
packet 0
packet 1
packet 2
ACK 1
ACK 2
ACK 0
3
packet 3
packet 4
packet 5
6
ACK 5
ACK 3
ACK 4
6
0
1
4
6
Without cumulative ACKs:
timeout & retransmission
With cumulative ACKs:
ACK 5 confirms everything up to 5

## Slide 44: Sliding Window
Stored packets at the sender
the sender must store all unacknowledged packets and be able to retransmit
maximum number defined by sender’s window size (here 3)
the packets not yet acknowledged by the receiver
Stored packets at the receiver
not necessary to store any packets
  receive buffer must hold at least one packet, but can be passed to next layer right away
not useful to store more than one receiver window size
ACK sent by receiver only if the packet
has been identified as being correct
can be transmitted correctly to the application
  correct includes “in the right order”
  correct includes usually: free from detected bit errors

## Slide 45: Transport layer
Flow Control: retransmission
IN2140: Introduction to Operating Systems and Data Communication

## Slide 46: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
ACK 0
packet 3
packet 1
packet 2
ACK 3
ACK 1
packet 3
ACK 2
discard 2
discard 3
This approach is called
Go-Back-N
Receiver accepts packets only in order
Advantages:
receiver needs only buffer for 1 packet
if the network usually looses >1 packets in a row, this fixes the problem quickly
packet 4

## Slide 47: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
ACK 0
packet 3
packet 1
packet 2
ACK 3
ACK 1
packet 3
ACK 2
sender
receiver
packet 0
packet 1
packet 2
packet 3
packet 1
ACK 3
ACK 0
ACK 0
ACK 0
packet 4
packet 4
keep 2
keep 3

## Slide 48: Sliding Window
Retransmission approaches
sender
receiver
packet 0
packet 1
packet 2
packet 3
packet 1
ACK 3
ACK 0
ACK 0
ACK 0
packet 4
This approach is called
Selective Repeat
Receiver buffers packets that arrive out of order but in window
Advantages:
less traffic
if the network usually looses only 1 packet in a row, this uses bandwidth better
keep 2
keep 3

## Slide 49: Transport layer
Flow Control
IN2140: Introduction to Operating Systems and Data Communication

## Slide 50: Flow Control on Transport Layer
Flow control mechanisms:
Stop-and-wait
Sliding window
  Go-back-N / no buffer allocation
  Selective repeat / static buffer allocation
  Credit mechanism / dynamic buffer allocation
Network
Layer
Transport
Layer
Application
Layer
Data Link
Layer
Physical
Layer
Fast sender shall not flood slow receiver
Link layer
Few connections (one per host)
Short distances
Transport layer
Potentially many connections (several per application)
Potentially long distances

## Slide 51: Transport layer
Flow Control:
sequence number space
IN2140: Introduction to Operating Systems and Data Communication

## Slide 52: Sliding Window: Go-Back-N
Example: sender: error detection by timeout
© Ralf Steinmetz, Technische Universität Darmstadt

## Slide 53: Sliding Window: Go-Back-N
Example for incorrect window size:
  amount of sequence numbers 8
  window size 8
  all ACKs lost
Correlation between
window size and
number of possible sequence numbers
 at least max. window size strictly less than range of sequence numbers

## Slide 54: Sliding Window: Go-Back-N
Correlation between
window size and
number of possible sequence numbers
at least max. window size strictly less than range of sequence numbers
Example for correct window size:
amount of sequence numbers 8
window size 7
all ACKs lost
sender
receiver
LB
UB
0
7
seq 0
ACK 0
seq 1
ACK 1
seq 2
ACK 2
seq 3
ACK 3
seq 4
ACK 4
seq 5
ACK 5
seq 6
ACK 6
1
0
2
1
3
2
4
3
5
4
6
5
7
6
seq 0
ACK 0
7
6
receiver discards packet 0 and resends ACK 0
everything OK
Timeout

## Slide 55: Sliding Window: Go-Back-N
Correlation between
window size and
number of possible sequence numbers
at least max. window size strictly less than range of sequence numbers
Example for incorrect window size:
amount of sequence numbers 8
window size 8
all ACKs lost
sender
receiver
seq 7
ACK 7
LB
UB
0
0
seq 0
ACK 0
seq 1
ACK 1
seq 2
ACK 2
seq 3
ACK 3
seq 4
ACK 4
seq 5
ACK 5
seq 6
ACK 6
1
1
2
2
3
3
4
4
5
5
6
6
7
7
0
0
seq 0
ACK 0
1
1
receiver accepts new packet 0, sends ACK 0 for a ”new” packet with sequence number 0
Timeout

## Slide 56: Sliding Window: Selective Repeat
X
0
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again

## Slide 57: Sliding Window: Selective Repeat
X
X
1
0
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again

## Slide 58: Sliding Window: Selective Repeat
X
X
X
1
2
0
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again

## Slide 59: Sliding Window: Selective Repeat
X
X
X
X
1
2
0
3
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again

## Slide 60: Sliding Window: Selective Repeat
X
X
X
X
X
1
2
0
3
4
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again
no ACKs arrived at the sender
must wait for timeout

## Slide 61: Sliding Window: Selective Repeat
1
2
0
3
4
Timeout
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again
Timeout
0
1
Timeout
window has slid 5 steps, so new values 0 and 1 fit into the tail although old values 0 and 1 were never successfully ACKed
no values have been ACKed, so they are all retransmitted

## Slide 62: Sliding Window: Selective Repeat
1
2
0
3
4
1
2
0
3
4
5
6
7
Correlation between
window size and
number of possible sequence numbers
 max. window size <= 1/2 range of sequence numbers
Example for incorrect window size:
  amount of sequence numbers 8
  window size 5
  all ACKs are lost, and the packet that has been lost last is the first one to arrive at the receiver again
Timeout
0
1
X
X
X
5
6

## Slide 63: Go-back-N vs Selective Repeat – a clear choice?
Burst errors are rare
  Selective Repeat repeats exactly the missing/bad packet
  Go-back-N discards lots of safely arrived packets
Error-free transmission
  Selective Repeat senders must wait after sending ½ sequence number space packets
  Go-back-N senders must wait after sending sequence number space-1 packets
Burst errors are frequent
  Selective Repeat waits for a timeout for every packet separately
  Go-back-N recovers quickly after the first timeouts

## Slide 64: Transport layer
Flow Control:
credit mechanism
IN2140: Introduction to Operating Systems and Data Communication

## Slide 65: Credit Mechanism
Flow control
  Credit mechanism
Buffer reservation
  Receiver allocates buffers dynamically for the connections
  Allocation depends on the actual situation
Principle
  Sender requests required buffer amount
  Receiver reserves as many buffers as the actual situation permits
  Receiver returns ACKs and buffer-credits separately
    ACK: confirmation only (does not imply buffer release)
    CREDIT: buffer allocation
  Sender is blocked when all credits are used up

## Slide 66: Credit Mechanism
Dynamic adjustment to
  Buffer situation
  Number of open connections
  Type of connections
    high throughput: many buffers
    low throughput: few buffers

## Slide 67: Credit Mechanism
Sender: A
Receiver: B
time
time
<req 8 buffers>
<cred=4>
<seq=0, data=m0>
<seq=1, data=m1>
<seq=2, data=m2>
<ack=1, cred=3>
<seq=3, data=m3>
<seq=4, data=m4>
<seq=2, data=m2>
<ack=4, cred=0>
<ack=4, cred=1>
<ack=4, cred=2>
<seq=5, data=m5>
<seq=6, data=m6>
<ack=6, cred=0>
<ack=6, cred=4>
A wants 8 buffers
A has 3 buffers left
A has 2 buffers left
Message lost but A thinks it has 1 left
A has 1 buffer left
A has 0 buffer left, must stop
A times out and retransmits
A still blocked
A may now send next msg.
A has 1 buffer left
A is now blocked again
A still blocked
B grants messages 0-3 only
Message lost
B acknowledges 0 and 1
permits 2-4
Everything acknowledged
but no free buffers
B found a new buffer
somewhere
B acks everything but has
no buffer

## Slide 68: Transport layer
Flow Control:
TCP
IN2140: Introduction to Operating Systems and Data Communication

## Slide 69: TCP Flow Control
Variable window sizes (credit mechanism)
  Implementation
    The actual window size is also transmitted with each acknowledgement
    Permits dynamic adjustment to existing buffer
Destination Address
Source address
Time to live
Protocol
Header checksum
Identification
D
M
Fragment offset
Version
IHL
Type of service
Total length
PRE
ToS
Data
Options
Source port
Destination port
Sequence number
Piggyback acknowledgement
THL
THL – TCP header length
U: URG – urgent
A: ACK – acknowledgement
P: PSH – push
R: RST – reset
S: SYN – sync
F: FIN – finalize
F
Window
S
R
P
A
U
unused
Checksum
Urgent pointer
Options (0 or more 32 bit words)
Sequence number and
acknowledgements
Credit

## Slide 70: TCP Flow Control
“Sliding window” mechanism
Sequence number space is limited
sequence number up to 232 bytes
window up to 216 units
  originally: units = bytes
  today: Window Scale Option, multiply window with scale factor 2N bytes, with 0 ≤ N ≤ 14
Acknowledgement and sequence number
  Acknowledgments refer to byte positions
  Sequence numbers refer to the byte position of a TCP connection
Positive acknowledgement
  Cumulative acknowledgements
    Byte position in the data stream up to which all data has been received correctly
    Reduces overhead and adds tolerance to ACK loss
Notes: Make a formula for the number of bytes that can be in flight.
Use a second slide for it.

## Slide 71: TCP Flow Control
Sender
Receiver
time
time
2K / SEQ=0
ACK=2048 WIN=2048
2K / SEQ=2048
ACK=4096 WIN=0
ACK=4096 WIN=2048
1K / SEQ=4096
Application does
a 2K write
Application does
a 2K write
Sender could send 2K
but application does
only a 1K write
Sender is blocked
Sender is blocked
4K buffer
2K
Application reads 2K
2K
1K
2K