## Slide 1: Transport layer
Introduction to Congestion Control
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Congestion
Traffic
  All traffic from all sources
Persistent congestion
  Router stays congested for a long time
  Excessive traffic offered
Transient congestion
  Congestion occurs for a while
  Router is temporarily overloaded
  Often due to burstiness
Notes: DRAW A TOKEN BUCKET!!!

## Slide 3: Reasons for congestion
Two senders, two receivers
One router, infinite buffers
No retransmissions
Maximum utilization of the networks
Very long delays in case of congestion
Router with infinite buffers
C
C/2
packets/second
receveived by Iiout
packets/second sent from Iin
C/2
long term avg delay
packets/second sent from Iin
Average delay becomes ∞ because queue keeps growing forever

## Slide 4: Reasons for congestion
Two senders, two receivers
One router, finite buffers
No retransmissions
Router with finite buffers
C
C/2
packets/second
receveived by Iout
packets/second sent from Iin
C/2
packets/second sent from Iin
no packet losses, empty queue
queue fills up, packets get lost
delay
time
example
queue is filling up
queue is full
When ∑Iin exceeds C, Iout is missing some data
long term avg delay

## Slide 5: Reasons for congestion
Two senders, two receivers
One router, finite buffers
Retransmission of lost packets
Router with finite buffers
Data rate sent by the application
Higher data rate sent by the transport layer including retransmissions
C

## Slide 6: Reasons for congestion
Retransmission means that Iout receives all data that Iin sends
When there is loss, retransmission is happening, and I’in > Iout
Retransmission of delayed (but not lost) packets increases I’in above the perfect value, without increasing Iout
“Cost of congestion”:
  More work (retransmissions) for a desired throughput
  Useless retransmissions, some links transmit several copies of the same packet
Constant bitrate (non-bursty) traffic
In
time
C/2
other rates for In
C/2
no congestion
persistent
congestion
Notes: ASK QUESTIONS
BLACKBOARD !!!!!!!!!

## Slide 7: Reasons for congestion
Retransmission means that Iout receives all data that Iin sends
When there is loss, retransmission is happening, and I’in > Iout
Retransmission of delayed (but not lost) packets increases I’in above the perfect value, without increasing Iout
“Cost of congestion”:
  More work (retransmissions) for a desired throughput
  Useless retransmissions, some links transmit several copies of the same packet
Bursty traffic
In
time
C/2
C/2
ideal line
transient congestion
The share of retransmissions grows

## Slide 8: Conclusion
Protocols should implement congestion control
Congestion control algorithms:
  algorithms to adapt the offered load (I’n) to the capacity at the bottleneck router
There are quite many algorithms that can achieve this
  at several layers
We are going to look mainly at TCP’s approach to congestion control

## Slide 9: Transport layer
Congestion Control in TCP
IN2140: Introduction to Operating Systems and Data Communication

## Slide 10: Global congestion collapse
Craig Partridge, Research Director for the Internet Research Department at BBN Technologies:
  Bits of the network would fade in and out, but usually only for TCP. You could ping. You could get a UDP packet through. Telnet and FTP would fail after a while. And it depended on where you were going (some hosts were just fine, others flaky) and time of day (I did a lot of work on weekends in the late 1980s and the network was wonderfully free then).
  Around 1pm was bad (I was on the East Coast of the US and you could tell when those pesky folks on the West Coast decided to start work...).
  Another experience was that things broke in unexpected ways - we spent a lot of time making sure applications were bullet-proof against failures. (..)
  Finally, I remember being startled when Van Jacobson first described how truly awful network performance was in parts of the Berkeley campus. It was far worse than I was generally seeing. In some sense, I felt we were lucky that the really bad stuff hit just where Van was there to see it.

## Slide 11: Internet congestion control: history
around 1986: first congestion collapse
1988: "Congestion Avoidance and Control" (Jacobson) Combined congestion/flow control for TCP (also: variation change to RTO calculation algorithm)
Idea: packet loss = congestion, so throttle the rate; increase otherwise
Goal: stability - in equilibrum, no packet is sent into the network until an old packet leaves
  ack clocking, “conservation of packets“ principle
  made possible through window based stop+go - behaviour
Superposition of stable systems = stable  network based on TCP with congestion control = stable

## Slide 12: TCP Congestion Control
TCP limits sending rate as a function of perceived network congestion
  little traffic – increase sending rate
  much traffic – reduce sending rate
Congestion algorithm has three major “components”:
  additive-increase, multiplicative-decrease (AIMD)
  slow-start
  reaction to timeout events

## Slide 13: TCP Congestion Control Algorithms
0
1
2
3
4
5
6
7
8
9
197x
198x
199x
200x
201x
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
TCP
TCP Tahoe
TCP Reno
TCP New Reno
TCP Vegas
TCP BIC
TCP Cubic
TCP Westwood
TCP Westwood+
Compound TCP
TCP PRR
TCP BBR
TCP Prague
the original TCP had no congestion control

## Slide 14: TCP Congestion Control
Basic terms:
congestion window (cwnd)
  largest amount of data (of a connection) that can be in the network at a time
maximum segment size [MSS]
  largest number of bytes that a TCP entity sends at once
  always in IPv6 and usually in IPv4: largest payload that fits into an IP packet behind the TCP header
  TCP header size is minimal 20 bytes
  with options maximal 60 bytes
Testing for available bandwidth
  Ideally: send as fast as possible (cwnd as large as possible) without loss
  Increase cwnd until you have loss
  If loss, reduce cwnd, try increasing again

## Slide 15: TCP Congestion Control
End-to-end control (no support from the network layer)
Send rate is limited by the size of a congestion window, cwnd (counted in bytes)
cwnd bytes can be sent in each RTT:
very often the permitted bytes are sent in packets
already
ack’d
sent, not
ack’d yet
sendable, not
sent yet
not sendable
yet
cwnd

## Slide 16: TCP Congestion Control
sender
receiver
Initially, cwnd size is a few MSS in this example: 1 MSS
round 1
round 2
round 3
round 4
sent packets per round (cwnd)
time
16
8
4
2
1
Then, the size increases by 1 for each received ACK (until threshold ssthresh is reached or an ACK is missing)

## Slide 17: TCP Congestion Control
16
8
4
2
1
Historically, initial ssthresh was 65 K, now in Linux it starts with ∞
sent packets per round (cwnd)
time
40
20
10
5
80
15
30
25
35
75
55
45
50
65
60
70
Losing a packet (TCP Tahoe):
ssthresh drops to half cwnd
cwnd back to 1
Losing a single packet (TCP Reno):
ssthresh drops to half cwnd
cwnd back to new threshold
ssthresh
ssthresh
50%
Notes: Why infinite ssthresh – try to get networking to work with a wide variety of bandwidth: 64 kbps modem in bad phone or countryside houses -> 10 GBps at IFI
Get to the right speed quickly !

## Slide 18: TCP Congestion Control
sent packets per round (congestion window)
time
40
20
10
5
80
15
30
25
35
75
55
45
50
65
60
70
ssthresh
ssthresh
Slow-start phase
Congestion avoidance
phase
Multiplicative Decrease
Performed when loss is detected in slow-phase and in congestion avoidance phase
Additive Increase
One more segments sent after 1 RTT without loss in congestion avoidance phase
Slow Start
TCP will always return to a slow start when a packet loss is detected by timeout (instead of duplicate ACKs). That means that it starts from scratch with only one segment per RTT, then 2, then 4, etc.
Today smallest
cong. window can
be as big as 10
(thanks to Google)

## Slide 19: TCP Fairness
Goal of fairness
  When N TCP streams share a bottleneck, each TCP stream should receive an nth of the bottleneck bandwidth
more realistic demand
  When N TCP streams with the same RTT and loss rate share a bottleneck, and they are infinitely long, each TCP stream receives an nth of the bottleneck bandwidth
but the approximation is in many cases good

## Slide 20: TCP Congestion Control
How does the AIMD algorithm achieve congestion control?
  interpret every packet loss as a congestion signal
  force TCP entities to slow down when loss is experienced
same share of bandwidth
throughput of stream 1
throughput of stream 2
stream 1 can increase BW consumption
stream 2 is backing off
consumes less than its share
stream 1 has experienced loss
backs off,
stream 2 can increase BW consumption
available bandwidth

## Slide 21: CUBIC: a new shape
use a cubic function for probing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 22: TCP New Reno
time
cwnd
classical
«sawtooth pattern» in
Additive increase multiplicative decrease phase

## Slide 23: TCP CUBIC

## Slide 24: TCP CUBIC
initial Wmax : slow start like in New Reno
Concave region
Convex region

## Slide 25: TCP CUBIC
The Window is a cubic function of the time since the last congestion event
CUBIC does not rely on receiving ACKs to increase window size
  Depends on on last congestion event
  CUBIC is better for long-distance connections, not for short-distance ones
  Use TCP New Reno behaviour for short-distance ones

## Slide 26: TCP CUBIC
C is a scaling factor
t is the elapsed time from the last window reduction
β is a constant multiplication decrease factor
cwnd grows rapidly
cwnd grows rapidly
cwnd grows slowly

## Slide 27: TCP CUBIC
cwnd grows rapidly
cwnd grows rapidly
cwnd grows slowly
Good for scaling
Good for stability
But: CUBIC converges slower than New Reno when flows appear or disappear

## Slide 28: Transport above transport
QUIC
Quick UDP Internet Connections
IN2140: Introduction to Operating Systems and Data Communication

## Slide 29: QUIC’s mission
Replace HTTP over TCP as the main protocol for web traffic
TCP’s problems
  Head of line blocking
  3-way handshake
  Small initial congestion window and slow start
  Large backoff caused by packet loss
  Small socket buffer
  NAT timeout and IP roaming
  TCP buffer block
  Security: TLS (transport layer security) is expensive

## Slide 30: QUIC’s mission
HTPP
IPv4/v6
TCP
UDP
TLS
QUIC
Ecryption, authentication
Session establishment, flow control, error correction,
congestion control

## Slide 31: QUIC goals
Transport layer tasks
Low latency
  In connect and responses
Reliable stream support
  Like TCP
  But without head-of-line blocking
Better congestion avoidance than TCP
  Keep experimenting! This is in user space
Session layers tasks
Privacy and security comparable to TLS
  Always end-to-end connection
  No benefits from caching
Mobile interface migration
Deploy in today’s Internet

## Slide 32: QUIC protocol header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|S| Unused | Version |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Version | DstCon ID len | Dest Conn ID 0-2040 bytes |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SrcCon ID len | Sec Conn ID 0-2040 bytes |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload ...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Very long and very flexible header
It is an application-layer protocol specifically targeting Chrome and Google servers
It can change every day on both sides

## Slide 33: QUIC’s congestion control: BBR
Searching for the ideal bandwidth
Assume that there is no competion
(ignore the competition)

## Slide 34: QUIC’s congestion control: BBR
Searching for the ideal bandwidth
Exponential search for good bandwidth

## Slide 35: QUIC’s congestion control: BBR
Searching for the ideal bandwidth
Drain excessive queue created during search

## Slide 36: QUIC’s congestion control: BBR
Searching for the ideal bandwidth
Loop: explore if more BW available, drain queue

## Slide 37: QUIC’s congestion control: BBR
Searching for the ideal bandwidth
Send really little for a short time
Give other flows a chance