## Slide 1: Network layer
Routing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Network layer
Routing - repetition
IN2140: Introduction to Operating Systems and Data Communication

## Slide 3: Network Layer
Primary task from a layer model perspective
  To provide service to the transport layer
    Connectionless or connection-oriented service
    Uniform addressing
    Internetworking: provide transitions between networks
    Routing
    Congestion control
    Quality of Service (QoS)

## Slide 4: Routing
The main L3 task is
  enable data transfer from end system to end system
    several hops, (heterogeneous) subnetworks
    compensate for differences between end systems during transmission
The Intermediate Systems are often called Routers
intermediate system
network
end system
network
is sub-network (subnet) of
routing depends on actual connections between intermediate systems (routers)
in many case, the organization into subnetworks coincides with routing borders and provides clues
but it is not essential for routing
routing algorithms work on graphs

## Slide 5: Inside the Network Layer
An L3 packet includes
Version
DSCP
Flow label
Payload length
Next header
Hop Limit
Destination Address
(128 bit)
Source address
(128 bit)
IPv6 Header
L4 Data
ECN
headers and trailer to specify service requirements
in particular:
information required by intermediate systems for forwarding
for connectionless service:
end system address of the destination
for connection-oriented service:
route label
OR
virtual circuits require routing during connection setup
route label is used later
packet switching requires routing for every packet
destination address is used for every packet

## Slide 6: Network layer
Routing - foundations
IN2140: Introduction to Operating Systems and Data Communication

## Slide 7: Routing: Foundations
Task
  To define the route of packets through the network
    From the source
    To the destination system
Routing algorithm
  Defines on which outgoing line an incoming packet will be transmitted
Route determination
  Packet
    Routing algorithm makes individual decision for each packet
  Virtual circuit
    Routing algorithm runs only during connect (session routing)

## Slide 8: Routing: Routing and Forwarding
Incoming
lines
Outgoing
lines
Router
IS
ES
ES
ES
ES
selecting an outgoing line

## Slide 9: Routing: Routing and Forwarding
Distinction can be made
  Routing: makes decision which route to use
  Forwarding: what happens when a packet arrives
desti-
nation
link
A
0
B
2
C
1
D
2
Routing
Process
Topology, link utilization, etc.
information
Fills & Updates
Uses & Looks up
Data packets
Incoming
lines
Outgoing
lines
Forwarding
Process
Routing
table
Router

## Slide 10: Good Properties for Routing Algorithms
Correctness
Simplicity
  Minimize load of ISes
Robustness
  Compensation for IS and link failures
  Handling of topology and traffic changes
Stability
  Consistent results
  No volatile adaptations to new conditions
Fairness
  Among different sources compared to each other
Optimality

## Slide 11: Routing Algorithms: Conflicting Properties
Often conflicting: fairness and optimization
Some different optimization criteria
  average packet delay
  total throughput
  individual delay
    conflict
Example:
  communication among a  A, b  B, c  C uses full capacity of horizontal line
  optimized throughput, but
  no fairness for x  X – Tradeoff between fairness and optimization
Therefore often
  hop minimization per packet
    it tends to reduce delays and decreases required bandwidth
    also tends to increase throughput
a
A
IS
IS
b
B
IS
IS
c
C
IS
IS
x
X

## Slide 12: Classes of Routing Algorithms
  Current network state not taken into consideration
    Assume average values
    All routes are defined off-line before the network is put into operation
    No change during operation (static routing)
  With knowledge of the overall topology
    Spanning tree
    Flow-based routing
  Without knowledge of the overall topology
    Flooding
  Decisions are based on current network state
    Measurements / estimates of the topology and the traffic volume
  Further sub-classification into
    Centralized algorithms
    Isolated algorithms
    Distributed algorithms
[Inkowik@wikipedia, CC BY SA 2.0]
[Ingolfsson@wikipedia]
Class: Non-adaptive Algorithms
Class: Adaptive Algorithms
Notes: Inkowik@wikipedia -

## Slide 13: Optimality Principle and Sink Tree
Starting idea: using a route has a cost
  number of hops, delay, …
General statement about optimal routes
  if router J is on the optimal path from router I to router K
  then the optimal path from router J to router K uses the same route
Idea of the proof
  best route from I to K is like this:
    r1: from I to J, then
    r2: from J to K
  then r2 is also the best route from J to K
  if better route r3 from J to K would exist
    then concatenation of r1 and r3 would improve route from I to K
Set of optimal routes
  from all sources
  to a given destination
  form a tree rooted at the destination: Sink Tree
I
J
K
r1
r2
r3

## Slide 14: Sink Tree
B
C
J
E
D
F
K
M
L
I
N
O
H
Sink Tree for Destination B
A
G
D
H
I
E
B
C
J
F
K
L
M
N
O
B
0
A
1
C
1
F
2
D
2
I
2
J
2
N
3
H
3
E
3
G
3
K
3
L
4
O
4
M
4

## Slide 15: Sink Tree
Sink Tree for Destination B
[Adrian Michael@Wikipedia, CC BY 3.0]
B

## Slide 16: Sink Tree
Sink Tree for
Destination B
B
C
J
E
D
F
K
M
L
I
N
O
H
A
G
D
H
I
E
B
C
J
F
K
L
M
N
O
Not realistic to use Sink Trees as real-life routing algorithm
need complete information about topology
Sink Tree is only a benchmark for routing algorithms
Goal of all routing algorithms
discover and use the Sink Trees for all routers
Comments
tree: no loops
  each optimal route is finite with bounded number of hops
not necessarily unique
  other trees with same path lengths may exist

## Slide 17: Methodology & Metrics
Compute the shortest path between a given pair of routers
Different metrics for path lengths can be used
  can lead to different results
  sometime even combined
Metrics for the «ideal» route
e.g. A «short» route
Bandwidth
Average data volume
Cost of communication
Delay in queues
...
Geographical distance
Number of hops

## Slide 18: Network layer
The Dijkstra Algorithm
or
Dijkstra’s Shortest Path First Algorithm
IN2140: Introduction to Operating Systems and Data Communication

## Slide 19: Non-Adaptive Routing
Shortest Path Routing

## Slide 20: Non-Adaptive Shortest Path Routing
Static Procedure
  Network operator generates tables
  Tables
    Are loaded when IS operation is initiated and
    Will not be changed any more
Characteristics
    Simple
    Good results with relatively consistent topology and traffic
  But
    Poor performance if traffic volume or topologies change over time

## Slide 21: Non-Adaptive Shortest Path Routing
Spanning Tree and Optimized Route
  Information about the entire network has to be available
    i. e. application actually as a benchmark comparison
Example
  Link is labeled with distance / weight
  Node is labeled with distance from source node along best known path (in parentheses)
  Find the shortest path from A to D
A
B
C
D
E
F
G
H
2
7
2
2
6
1
2
4
3
3
2
A
B (●,-)
C (●,-)
D (●,-)
E (●,-)
F (●,-)
G (●,-)
H (●,-)

## Slide 22: Non-Adaptive Shortest Path Routing
Procedure: e. g. according to Dijkstra
Find the shortest path from A to D
  Labels may be permanent or tentative
  Initially, no paths are known
    All nodes are labeled with infinity (tentative)
  Discover the labels that represent shortest possible path from source to any node
  Make those labels permanent
  1. Node A labeled as permanent (filled-in circle)
  2. Relabel all directly adjacent nodes with the distance to A (path length, nodes adjacent to source)
  3. Examine all tentatively labeled nodes, make the node with the smallest label permanent
  4. This node will be the new working node for the iterative procedure (i.e., continue with step 2.)

## Slide 23: Non-Adaptive Shortest Path Routing
Procedure: e. g. according to Dijkstra
Find the shortest path from A to D:
  A flagged as permanent (filled-in circle)
  Relabel all directly adjacent nodes with the distance to A
    (path length, IS adjacent to the source):
2
7
2
2
6
1
2
4
3
3
2
A
B (●,-)
C (●,-)
D (●,-)
E (●,-)
F (●,-)
G (●,-)
H (●,-)
B (2,A)
G (6,A)

## Slide 24: Non-Adaptive Shortest Path Routing
Procedure: e. g. according Dijkstra
Find the shortest path from A to D:
  ...
  Compare all recent, not firmly flagged IS;
    flag the one with the lowest number as fixed
  This IS is the origin of the iterative procedure
    (i. e. continue with item 2.)
2
7
2
2
6
1
2
4
3
3
2
A
C (●,-)
D (●,-)
E (●,-)
F (●,-)
H (●,-)
B (2,A)
G (6,A)

## Slide 25: Non-Adaptive Shortest Path Routing
Procedure: e.g., according to Dijkstra
Find the shortest path from A to D:
  Node B has been labeled as permanent (filled-in circle)
  relabel all directly adjacent nodes with the distance to B (path length, nodes adjacent to source):
    A (does not apply, because it is the origin),
2
7
2
2
6
1
2
4
3
3
2
A
C (●,-)
D (●,-)
F (●,-)
H (●,-)
B (2,A)
E (4,B)
G (6,A)
C (9,B)
E (●,-)

## Slide 26: Non-Adaptive Shortest Path Routing
Procedure: e.g., according to Dijkstra
find the shortest path from A to D:
  …
  …
  examine all tentatively labeled nodes;
    make the node with the smallest label permanent
  this node will be the new working node for the iterative procedure ...
2
7
2
2
6
1
2
4
3
3
2
A
D (●,-)
F (●,-)
H (●,-)
B (2,A)
C (9,B)
E (4,B)
F (6,E)
G (6,A)
H (9,G)
G (5,E)
D (10,H)
H (8,F)

## Slide 27: Non-Adaptive Shortest Path Routing
An alternative approach to Dijkstra’s algorithm
A
B
C
D
E
F
G
H
2
7
2
2
6
1
2
4
3
3
2
A
B
C
D
E
F
G
H
A
B
C
D
E
F
G
H
0A
2A
6A
A
9B
4B
B
6E
5E
E
6E
9G
G
9B
8F
F
9B
10H
H
10H
C

## Slide 28: Non-Adaptive Shortest Path Routing
An alternative approach to Dijkstra’s algorithm
A
B
C
D
E
F
G
H
0A
2A
6A
A
9B
4B
B
6E
5E
E
6E
9G
G
9B
8F
F
9B
10H
H
10H
C

## Slide 29: Non-Adaptive Shortest Path Routing
An alternative approach to Dijkstra’s algorithm
A
B
C
D
E
F
G
H
0A
2A
6A
9B
4B
6E
5E
6E
9G
9B
8F
9B
10H
10H
A
B
E
G
F
H
C
A
B
C
D
E
F
G
H

## Slide 30: Non-Adaptive Shortest Path Routing
A
B
C
D
E
F
G
H
B
B
B
B
B
B
B
A
B
C
D
E
F
G
E
E
E
E
E
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
G
-
H
-
-
-
-
H
-
-
-
-
-
-
-
A
B
C
D
E
F
G
H
A
B
C
E
F
H
D
-
-
-
-
-
-
A
C
D
B
E
F
G
H
Y reaches X through <cell>
Y
X
Build individual routing tables from tree
Perform a Depth First Search
leading to this visit sequence C D H F G E B A
{C}
{D}
{D,H}
{D,F,H}
{G}
{D,E,F,G,H}
{B,C,D,E,F,G,H}
C
F
F
F

## Slide 31: Network layer
Distributed Routing:
Link State Routing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 32: Link State Routing
A very frequently use routing protocol
  IS-IS (Intermediate System-Intermediate System)
  OSPF (Open Shortest Path First)
Basic principle
  IS measures the "distance" to the directly adjacent IS
  Distributes information
  Calculates the ideal route
Procedure
  Determine the address of adjacent IS
  Measure the "distance" (delay, ...) to neighbouring IS
  Organize the local link state information in a packet
  Distribute the information to all IS
  Calculate the route based on the information of all IS

## Slide 33: Link State Routing
1. Phase: gather information about the adjacent intermediate systems
A
F
B
C
LAN
D
E
G
H
I
A
F
B
C
D
E
G
H
I

## Slide 34: Link State Routing
1. Phase: gather information about the adjacent intermediate systems
A
F
B
C
LAN
D
E
G
H
I
N
A
F
B
C
D
E
G
H
I
Initialization procedure
New IS
  Sends a HELLO message over each L2 channel
Adjacent IS
  Responds with its own address, unique within the network

## Slide 35: Link State Routing
2. Phase: measure the "distance"
Definition of distance needed
  Usually delay
  Where to measure?
Uses & Looks up
Data packets
Incoming
lines
Outgoing
lines
Forwarding
Process
Routing
Process
Topology, link utilization, etc.
information
Fills & Updates
desti-
nation
link
A
0
B
3
C
1
D
4
Routing
table
Router
HELLO
ECHO
Queues
When to start timer?

## Slide 36: Link State Routing
2. Phase: measure the "distance“
Queuing delay
  Measuring without does not take load into account
  Measuring with does  usually better
But
  Possibility for oscillations (route flapping)
  Once per routing table update

## Slide 37: Link State Routing
3. Phase: organizing the information as link state packet
Including own address, sequence number, age, "distance"
Timing problems: validity and time of sending
  Periodically
  In case of major changes

## Slide 38: Link State Routing
4. Phase: Distributing the local information to all IS
By applying the flooding procedure
  Therefore, sequence number in packets
Problem: inconsistency
  Varying states simultaneously available in the network
  Indicate and limit the age of packet, i. e. IS removes packets that are too old
5. Phase: Computing new routes
Each IS for itself
Possibly larger amount of data available
Dijkstra’s algorithm is a popular choice
Very robust
But does not scale to large networks

## Slide 39: Link State Routing
Phase: gather information about the adjacent intermediate systems
Phase: measure the "distance“
Phase: organizing the information as link state packet
Phase: Distributing the local information to all IS
Phase: Computing new routes

## Slide 40: Network layer
Distributed Routing:
Distance Vector Routing
IN2140: Introduction to Operating Systems and Data Communication

## Slide 41: Distance Vector Routing
Principle
every IS maintains a table (i.e., vector) stating
  best known distance to destinations
  and line to be used
ISes update tables
  by exchanging routing information with their neighbors

## Slide 42: Distance Vector Routing
Each IS
  maintains routing table with one entry per router in the subnet
  is assumed to know the distances to each neighbor
  sends list with estimated distances to each destination periodically to its neighbors
X receives list E(Z) from neighbor Y
  Distance X to Y: e
  Distance Y to Z: E(Z)
  Distance X to Z via Y: E(Z)+e
IS computes new routing table from the received lists containing
  Destination IS
  Preferred outgoing path
  Distance
Y’s Estimate of its own distance to Z
X’s measurement of its own distance to Y

## Slide 43: Distance Vector Routing
Previous routing table will not be taken into account
  Reaction to deteriorations
A
B
C
D
E
F
G
H
I
J
K
L
A
0
B
12
C
25
D
40
E
14
F
23
G
18
H
17
I
21
J
9
K
24
L
29
A
24
36
18
27
7
20
31
20
0
11
22
33
I
20
31
19
8
30
19
6
0
14
7
22
9
H
21
28
36
24
22
40
31
19
22
10
0
9
K
28
20
17
30
18
0
15
8
A
20
A
I
H
I
I
H
12
H
10
I
-
6
K
K
line
JA
8
delay
JI
10
JH
12
JK
6

## Slide 44: Distance Vector Routing
Fast route improvement
Fast distribution of information about new short paths (with few hops)
A
B
C
D
E
∞
∞
∞
∞
1
∞
∞
∞
1
2
∞
∞
1
2
3
∞
1
2
3
4
Example
  initially A unknown
  later: A connected with distance 1 to B, this will be announced
  Distribution proportional to topological spread
  Synchronous (stepwise) update is a simplification

## Slide 45: Distance Vector Routing
Slow distribution of information about new long paths (with many hops)
“Count to Infinity” problem of DVR
Example: deterioration
  Here: connection destroyed
  A was previously known, but is now detached
  The values are derived from (incorrect) connections of distant IS
Comment
  Limit "infinite" to a finite value, depending on the metrics, e.g.
    ‘infinite’ = maximum path length+1
A
B
C
D
E
∞
∞
∞
∞
1
2
3
4
3
2
3
4
3
4
3
4
5
4
5
6
5
6
5
6
7
6
7
6
7
8
7
8

## Slide 46: Distance Vector Routing
Variant: ‘Split Horizon Algorithm’
Objective: improve the "count to infinity" problem
Principle
  In general, to publicize the "distance" to each neighbour
  If neighbor Y exists on the reported route, X reports the response "false" to Y
    distance X (via Y) according to arbitrary i: 
Example: deterioration (connection destroyed)
  B to C: A =  (real), C to B: A =  (because B is on path to A), ...
But: still poor, depending on topology, example
  Connection CD is removed
  A receives "false information" via B
  B receives "false information" via A
    Slow distribution (just as before)
A
B
C
D
E
1
2
3
4
∞
2
3
4
∞
∞
3
4
∞
∞
∞
4
∞
∞
∞
∞
A
B
C
D